## Slide 1: CS2100
Tutorial #4
Question 4
(Prepared by: Aaron Tan)

## Slide 2
5
4
5
2
8
5
6
3
Critical Path Analysis
Jobs in sequence/series
a
b
c
Duration = a + b + c
a
b
c
Jobs in parallel
Duration = max(a,b,c)
Critical path duration = 5 + 4 + 8 + 6 = 23
The Critical Path is the longest path from start to finish, indicating the minimum time necessary to complete the entire operation.
This path is critical as any delay along this path is going to delay the completion of the operation. Hence the critical path is the bottleneck route.
Applications in project management, allocation of resources, scheduling, etc.
What is the critical path for this graph? What is its duration?

## Slide 3
0
1
0
1
0
1
1
0
Q4(a)
SUB instruction
Inst-Mem (400)
Reg.File (200)
Control (100)
MUX (ALUSrc)
(30)
ALU
(120)
MUX (MToR)
(30)
Reg.File
(200)
Not on critical path
400+200+30+120+30+200 = 980ps
0
1
Inst-Mem
400ps
-------------
Adder
100ps
-------------
MUX
30ps
-------------
ALU
120ps
-------------
Reg-File
200ps
-------------
Data-Mem
350ps
-------------
Control/ALUControl
100ps
-------------
Lshft/Signext/AND
20ps
Why is MUX (RegSrc) not included?
Because WR is not needed at this moment.
Data memory not needed.

## Slide 4
0
1
0
1
0
1
1
0
Q4(b)
LW instruction
Inst-Mem (400)
Reg.File (200)
Control (100)
ALU
(120)
MUX (MToR)
(30)
Reg.File
(200)
Not on critical path
400+200+120+350+30+200 = 1300ps
Why is MUX (ALUSrc) (and Sign-extend) not included this time?
DataMem
(350)
Inst-Mem
400ps
-------------
Adder
100ps
-------------
MUX
30ps
-------------
ALU
120ps
-------------
Reg-File
200ps
-------------
Data-Mem
350ps
-------------
Control/ALUControl
100ps
-------------
Lshft/Signext/AND
20ps
MUX (RegSrc) not included. Same reason as (a).
Because Sign-extend and MUX(ALUSrc) are in parallel with Reg-File.
Reg-File = 200; Sign-ext + MUX = 20+30 = 50.